## Slide 2
The Intelligent Network Infrastructure
David Meyer
Chief Scientist
dmm@1-4-5.net

## Slide 3: Agenda
What can ML/AI bring to the network?
Huawei’s Approach: Intelligent Network Infrastructure
- Architecture and Impacts
- Key Technologies
- Case Studies
Roadmap

## Slide 4: Before We Dive In
What This Talk Is About
  Machine Learning [Focus on Networking]
  Solving Engineering Problems
  May be used by AGI
  Sometimes: Narrow or Weak AI
What This Talk Is Not About
  Artificial General Intelligence (AGI)
  Defn: An AGI is an intelligent machine that can successfully perform any intellectual task that a human being can
  Sometimes: Strong AI

## Slide 5
Many
Perhaps the most basic assumption/prior: Smoothness
BTW, What Assumptions Are We Making?
x close to x’  f(x) close to f(x’)
Multiple explanatory factors/distributed representations
Hierarchical organization of explanatory factors
Shared factors across tasks
Manifolds
Sparsity
Simplicity of Factor Dependencies
https://arxiv.org/pdf/1206.5538.pdf
Other Priors

## Slide 6: So What Can ML/AI Do For Networks?
Response Period
Visual field & Precision
Reactive Control
Dead Corner
Local
Distributed
Centralized
Chart: 
| Dynamicity | Proactivity | Data | Randomness | Automation
Current Ability | 0.4 | 0.42 | 0.45 | 0.5 | 0.37
Future Demand | 1 | 1 | 1 | 1 | 1
IP traffic is dynamic and bursty at any time scale (self-similarity/scale invariance)
Overprovisioning typical approach to QoS.
Coarse Control
Reactive control responds to events after the event occurs.
Need proactivity since reactive might be too late.
Reactive
Predictions are probabilistic and networks exhibit many different stochastic behaviors.
Typical approach to deal with ”noise”: Use the average, maximum, and variance to compute a (likely suboptimal) safety margin. Example: Overprovisioning vs. QoS
Wide & Static Safety Margin
Learning (data) will play more important roles in all network functions. As such we must design s/w and h/w for data export (but what format, what meta-data, etc).
Note: Dependence (correlation) does not imply causation. How then can we accomplish many of our primary tasks (e.g. root cause analysis) in a non-ad-hoc fashion?
Emerging
New and services (e.g. IoT) exceed the manual capacity.
Introducing ML/AI into network aims to improve automation (lots of runway)
Automation

## Slide 7: ML/AI Functionality For Networks
GOOD AT | VALUE
Solving Complex Problems | Dynamic Control Dynamically control the traffic both in overlay / underlay network and flow / packet level. Real-time and fine-grain policies.
Automated Decision-Making | Lower OPEX Automated decision-making simplifies the operations.
Mining and Modeling | Enable More ML enable various forms inference which can be used to proactively guarantee the QoS and QoE.

## Slide 8: Lots of work trying to bring ML to networking
  Routing
    “Self-Aware Networks: the Cognitive Packet Network and its Performance”
    “Towards a cognitive routing engine for software defined networks”
    Note: Distance vector routing vs. TD(0) learning
  Traffic Engineering
    “RLTE: Reinforcement Learning for Traffic-Engineering”
    “Experience-driven Networking: A Deep Reinforcement Learning based Approach”
  Resource Management
    “Resource Management with Deep Reinforcement Learning”
  Congestion Control
    “TCP ex Machina: Computer-Generated Congestion Control”
    “An experimental study of the learnability of congestion control”
    https://www.ietf.org/proceedings/101/slides/slides-101-iccrg-pcc-performance-oriented-congestion-control-00.pdf
 | Rollout
1 | Best Effort: No traffic optimization
2 | Traditional TE: Use static policy to optimize traffic.
3 | Open Loop Control: Based on stage 2, implement traffic monitoring and recognition. Manually make the policies and adjust the network configuration in period.
4 | Closed Loop Control: Based on stage 3, some (but not all) network policies can be deployed and executed automatically and others retain human decision-making (e.g. via recommender systems)
5 | Autonomous Networking: Based on stage 4, all the network policies can be deployed and executed automatically. Again, retain open loop control

## Slide 9: Agenda
What can ML/AI bring to the network?
Huawei’s Approach: Intelligent Network Infrastructure
- Architecture and Impacts
- Key Technologies
- Case Studies
Roadmap

## Slide 10: Architecture
AI
Control
Embedded
AI
Forwarding
INI Network Node
Data Mng
Collection
Cleaning
Training Data Set
AI Platform
AI
Data Process
AI Platform
Data Mng
Training Data Set
AI
Mng
Management
Plane
Control
Plane
Collection
Plane
Forwarding
Plane
Measurement
AI
Control
AI
Data Process
AI
Mng
A new plane: Data Collection Plane
  Data measurement, collection and process
  Serving three planes (Control, Management, Forwarding)
Modeling
Alg
Control Alg
Model
Control actions
Control APPs
Eval Alg
Action
Dispatch
Status
Collection
Network Status
Management
Plane
Control
Plane
Collection
Plane
Complement

## Slide 11: Impact on Control Plane
IMPACT | FROM | TO
Data-driven self-learning | human study & design | learn from data, optimize ops
High frequency operations for real-time optimization | manually adjustment in months | automatic operation in seconds (or less)
Emerging of self-shaping control protocols | human designed protocols | agents develop optimized communication protocols (Example: Google Translate’s use of NTMs, interlingua)
BTW, what is the difference between dependence (e.g. correlation) and causality, and can you learn causal relationships from non-experimental observations?

## Slide 12
IMPACT | FROM | TO
Data-driven self-learning | human study & design | algorithms learn from data
Human interfaces | all the details | hide details and only provide KPIs
Information type | historical statistics, current status monitoring, tons of logs | summarized, analyzed, predicted report
When we observe some data, what are we really observing?
The joint distribution over the variables of interest,
is called the Data Generating Distribution (DGD)
Impact on Management Plane
W

## Slide 13: Impact on Forwarding Plane
IMPACT | FROM | TO
Data measurement requirement | Limited data measurement | More data measurement needed
Forwarding mechanism | Forwarding mechanism matching current control system， Example: ACLs configured manually in many cases | New control system e.g. traffic balancing in forwarding procedure according to specified percentage of each next hop in routing table
ML assisted forwarding plane | Reactive/Preset resource reservation | predictive resource allocation
BTW, under what conditions can we be “predictive” (and what does predictive even mean)?

## Slide 14: Emergence of the “Collection” Data Plane
As with the network and service complexity increases, data will play an increasingly important role
- Data collection is a complex and heavy load work. It needs careful organization and design.
- Support multi-layers
- Functions: network state measurement, centralized or distributed, planning/optimization/compression of measurement.
Small-scale
Aggregation
DB
Data Plane
Small-scale. Feedback and reactive when necessary.
Middle-scale. Data become a set of network states. Support the local controller functions
Large-scale. Data become an abstract of lower infrastructure and services. Become an independent and global view of network
Data
Data
Data
Data
Data
Data
Distributed
Large-scale
Aggregation

## Slide 15: Agenda
What can ML/AI bring to the network?
Huawei’s Approach: Intelligent Network Infrastructure
- Architecture and Impacts
- Key Technologies
- Case Studies
Roadmap

## Slide 16: Modern ML: Theory + Engineering
Theory
  Reinforcement learning to learn control (actions). Contrast inference (regression, classification, …)
  Stochastic modeling & variational inference: Variational AutoEncoders，Bayesian Networks
  Hierarchical/multi-layer Control
  Self-shaping protocols
  Temporal prediction (RNNs such as LSTM, etc)
Engineering
  Open loop control (e.g. recommender system), digital twins, threshold limitation, online-learning …
  Rapid learning: limit the impact of the learning phase (for example, low-shot learning)
  Scalability
  Forwarding plane ML
  Efficient data collection: Selective data measurement, telemetry
What is the ”effective distance” between theory and practice in ML these days?

## Slide 17: Agenda
What can ML/AI bring to the network?
Huawei’s Approach: Intelligent Network Infrastructure
- Architecture and Impacts
- Key Technologies
- Case Studies
Roadmap

## Slide 18: Case Study 1: Intelligent Traffic Balancing
AI
controller
Data
collector
AI + TE
Data
Learning
Inference
Controller
Ctrl Loops
CORE
AGG
ACC
MAN (Metro Area Network)
____Goal
Congestion avoidance.
Real-time load balancing.
Improving QoS
____Solution
Multi-path route computation by traditional graph algorithms, for each Ingress-Egress pair.
Online Reinforcement Learning algorithm adjusts traffic distribution at every router to multiple outgoing ports. What would a reward function look like?
Modified forwarding plane forwards packet according to the percentage in flowlets to keep packet order
____Benefit
Reducing Max-Link-Utilization by 23% (vs ECMP)
Reducing data loss by 64% (vs ECMP)
Reducing link delay by 19% (vs ECMP)
Achieves performance close to both MLU and packet loss with CONGA (ms-level distributed control) using second-level centralized control.
Automatically adapts to evolving traffic pattern and network status

## Slide 19
Case Study 2: Intelligent Overlay Routing
AI + SD-WAN
End-to-End Quality
Traffic Rerouting
ISP networks are black-boxes to users.
Routes, link status are changing and unknown.
Only end-to-end quality is measureable.
Probe
____Problem
Underlying networks are black-boxes
WAN path quality keeps changing, only partially predictable
Optimal leased-line/VPN traffic routing is based on estimated path quality
____Solution
Online Reinforcement Learning algorithm provides adaptive routing from dynamic path quality
Multiple objective: Delay, jitter, dropping, cost
Data
Learning
Inference
Controller
Ctrl Loops
____Benefit
30% average delay improvement over test bed (vs D-ECMP)
Automatically adapts to evolving status of underlying networks
Delay
~0.2ms
~50ms
Packet Loss
Traffic
Probability Distribution
of Delay

## Slide 20: Case Study 3: QoS Inference Engine
Human
(Open Loop)
LSTM:
Traffic feature extraction
VAE:
QoS distribution reconstruction
QoS Inference Engine
Collect traffic matrix
along time
Infer QoS distribution
Network QoS (delay,jitter, loss…)
Precise Network Capacity Planning
Real-time QoS Monitoring & Anomaly Detection
Smarter AI design
with QoS prediction
Inference
Reliable AI control for SLA guarantee
  Achieve millisecond-level QoS response based on generative ML algorithms
  Self-learning directly from historical traffic; Achieve automatic inference of full probability distribution as opposed to point estimates.
Supports customizable QoS models (e.g., delay, jitter and loss); Enable real-time SLA guarantees throughout the network, including quasi-real time QoS monitoring and anomaly detection. What is anomaly detection and how might you do it?
Applications
AI Controller
(Close Loop)
AI + Modeling
Data
Learning
Inference
Controller
Ctr Loops

## Slide 21: Aside: What is an Autoencoder?
MNIST: 28x28 Grayscale Handwritten Digit Dataset
Training set: 55000 images
Test set: 10000 images
Validation set: 5000 images
Features here are pixels (28x28 = 784)
To understand what an autoencoder is, we need a data set
Why MNIST? I thought we were talking about networks… Well, I’m using MNIST here because you can easily visualize what is going on. In our case, instead of the input being vectors of {0,1} we will have vectors of counters of various features s/a bandwidth, and other network and host based metrics/KPIs.

## Slide 22: Autoencoder? Special Kind of Neural Network
Key Characteristic: Hidden layer has fewer units than input/output  Compression
Goal: Minimize reconstruction (decode) error
  How to define error (loss, cost)?
  Binary classification: Threshold reconstruction error  normal/abnormal
Unsupervised learning
784
784
100

## Slide 23: But First: What Does A Single Neuron Do?
Inner (dot) Product
How many parameters?
784
784
100
784x100 + 100x784 = 156800
Sigmoid/logistic Function

## Slide 24: So What Kinds of Things Can a Single Artificial Neuron Compute?
Graphic courtesy Hugo Larochelle
Can Solve Linearly Separable Problems

## Slide 25: So What is Really Happening Here?
Voronoi diagram under Euclidian distance
Linear Separability in a Neural Network
Voronoi diagram under Euclidian distance
Linear Separability in a Neural Network
Deep Nets disentangle the underlying explanatory factors in the data so as to make them linearly separable
Graphic courtesy Christopher Olah
Linear Decision Boundary
Target function represented by input data is some twisted up manifold

## Slide 26: Manifolds?
X is a high dimensional vector (MNIST: 282 = 784)
Data concentrated around a lower dimensional manifold
Hope is to find representation of that manifold
Graphic courtesy http://www.deeplearningbook.org

## Slide 27: So OK, All Cool, But How Does The Autoencoder Actually Work?
But First: What do we need to assume?
Independent Identically Distributed (iid) data
What does this mean? The joint distribution factorizes.
Suppose we have T samples. Then iid 
Learning comes down to adjusting the weights (wi’s) so that the loss L(x,r) is minimized. This is the job of backpropagation (calculate the gradients) and gradient descent (find the minima of the loss function).

## Slide 28: How Hard To Code This Up In Tensorflow?
https://github.com/davidmeyer/ml/blob/master/tensorflow/autoencoder.{py,ipynb}

## Slide 29: Autoencoder Output
1 example
10 examples
100 examples
1000 examples
After training, the AE gets low reconstruction error on digits from MNIST and high reconstruction error on everything else: It has learned to recognize MNIST

## Slide 30: Aside: How Big is the MNIST Space?
So how many 28x28 grayscale images are there?
Say there are 8 bits of grayscale  256784 possible 28x28 “images”
Our autoencoder had 156800 parameters  156800/256784
So how can a simple autoencoder find the MNIST subspace?
One (physics) perspective: http://arxiv.org/pdf/1608.08225v1.pdf

## Slide 31: Case Study 4: Intelligent Measurement
Data-driven
Addresses the data requirement for ML applications
Visualization network performance
Scale
Intelligent measurement
Data recovery via matrix completion by measuring only 20% of node-pairs
Online schedule of measurement points based on matrix coherence feature
Performance improvement on latency measurement (Note that comparison 2 of uniform sampling is static with no online scheduling).
Selective measurement & recovery by Coherence-Based Sampling
Network
AI App & Others
20%
27%
25%
Data
Learning
Inference
Controller
Ctrl Loops
AI + Measurement

## Slide 32: Agenda
What can ML/AI bring to the network?
Huawei’s Approach: Intelligent Network Infrastructure
- Architecture and Impacts
- Key Technologies
- Case Studies
Roadmap

## Slide 33: Roadmap
Entry
Intermediate
Advanced
Separate ML/AI applications
e.g. Temporal prediction
Measurement Collection
Additional forwarding options
Probing
Centralized control
Separate ML/AI applications
Admin assistant
Causal analysis
Selective collection & completed by inference
Data cleaning
Separate optimized operations
e.g. predictive resource management
Centralized control +
Isolated distributed control
Global optimized
Policy assistant
Global optimized collection & inference
Intelligent prefetching
Service optimization @ wire speed
Integrated hierarchical control
Management
Plane
Control
Plane
Collection
Plane
Forwarding
Plane

## Slide 34: DEMO: #44 HUAWEI
Intelligent Network Infrastructure —— HUAWEI’s Practice on Network + AI Technologies
Learning
Inference
Intelligence
Data & Control
Device
- Best Status At Every Second
Optimizes traffic over networks in real-time, to be well balanced, congestion-free for optimal QoS.
- Automation & Adaptation
Automates and simplifies operations of network management in background of evolving traffic pattern and network construction.
SDN
Controller
Ctrl Loops
PROVIDE
Data
Collecter
- Optimal and guaranteed QoS
Proactively avoid the congestion, failure and potential problems so that to guarantee the QoS for customer’s services.

## Slide 35
Thanks!
Q & A